MANAGEMENT OF HEALTH AND SAFETY AT WORK REGULATIONS 1999

GENERAL RISK ASSESSMENT - FORM RA2

| DEPARTMENT/SCHOOL/UNIT | PHYSICS – Reigate Grammar School | REF NO. | RA 1000 |
| --- | --- | --- | --- |

| TASK/OPERATION BEING ASSESSED | Vacuum pumps and vacuumed objects |
| --- | --- |

PURPOSE/METHOD OF WORK

For: PHYSICS Purpose: Any lesson involving a vacuum, of any standard, especially when using the vacuum pump. Method: Ensure that the classroom and layout are appropriate for the type of lesson to be taught. Ensure that everyone is wearing protective glasses, the operator should only be a teacher wearing a lab coat and leather gloves. Ensure the valves on the pump are open to begin with and the venting tube leads outside. Ensure that before operation the glass dome is covered with the protective metal ‘basket’. Before evacuating a container, visually check for cracks, chips and any sign of weakness. If any are found, do not use. Check that adhesive tape has been attached to the outside of the glass. The evacuated object must at all times be kept behind a Perspex safety screen. Handle any evacuated objects with care. Keep evacuation time to a minimum. Once the experiment is over, make sure the vacuum pump is switched off and that valves are opened slowly on the pump and evacuated object to allow pressure to reach equilibrium.

| SPECIFIC LEGISLATIVE REQUIREMENTS |  | LEVEL OF SKILL/TRAINING REQUIRED |
| --- | --- | --- |
| Health & Safety at Work etc. Act Management of Health & Safety at Work Regulations Control of Substances Hazardous to Health Regulations Electricity at Work Regulations Personal Protective Equipment at Work Regulations Provision and Use of Work Equipment Regulations Workplace (Health, Safety & Welfare) Regulations |  | Qualified Teacher |

| CHEMICALS/MATERIALS INVOLVED | HSC NO. | ASSESSMENT DATE |  | SPECIFIC WORK EQUIPMENT PROVIDED |
| --- | --- | --- | --- | --- |
|  |  |  |  | Vacuum pump. Spherical glass flask. Long Galileo tube. |

| MAIN HAZARDS IDENTIFIED | WHO WILL BE AFFECTED | CONTROL MEASURES TO REDUCE THE RISK |
| --- | --- | --- |
| Implosion and flying glass leading to cuts and lacerations. Any piece of glassware under vacuum e.g. tubes, flasks, pipes and storage bulbs on vacuum lines, has the potential to do harm following implosion. The energy imparted to flying fragments is directly proportional to the volume of the glass vessel evacuated. It follows that the potential to do harm is also directly proportional to the volume of the glass vessel. It is a common misconception that so called "high vacuum" (typically 10-3 mbars or better) systems present a significantly greater hazard than everyday vacuums produced by e.g. a water pump (around 30 mbars). These may differ by four orders of magnitude but the forces to which the glassware is subjected is essentially the same i.e. High Vacuum, 99.999% of atmospheric pressure. Water Pump, 97% of atmospheric pressure. | Pupils and Teachers | Any sealed, evacuated glass vessel or any glass vessel about to be evacuated should be shielded using any of the methods described below. • Surround the vessel using a suitable container of wood, metal, plastic or heavy cardboard. (Clearly this method can be used only when the part of the apparatus to be shielded does not need to be visible.) • Stick transparent adhesive film, cut from a sheet or in tape form, to the glass. • Place safety screens between the apparatus and the spectators and between the apparatus and the operator, who should also wear eye protection. More information is available at: L:\CLEAPSS 2008\StartPC.exe.lnk Under pumps in section 10.6 |

| MANUAL HANDLING RISK |  | PERSONAL PROTECTIVE EQUIPMENT REQUIRED |
| --- | --- | --- |
| Has a manual handling risk been identified? YES The risk considered to be Low Is a further detailed assessment required? NO |  |  |
| If the answer to the above question is YES a separate manual handling assessment will be required to fulfil the requirements of the Manual Handling Operations Regulations 1992. |  | Is training and instruction required NO Is there need for special accommodation NO Is there need for test/examination Yes Is all P. P. E. compatible NO |

| FREQUENCY OF MONITORING |  | ASSESSMENT REVIEW PERIOD |
| --- | --- | --- |
| N/A | 3 Months | 6 Months | 1 Year | > 1 Year |  | < 1 Year | 2 Years | 3 Years | 4 Years | > 4 Years |

Signed ------------------------------------------------------------------------------------------	Post/Title ------------------------------------------------------------

Date ---------------------------------------------------------------------------------------------